A Manned Space Elevator
A Manned Space Elevator
Bradley C. Edwards
[Speaker Notes: Slides assembled by Brad Edwards. Please read the book The Space Elevator (Edwards and Westling, available at Amazon) prior to presenting so an understanding of the basic program can be understood.]

---
Issues Sending People up the Space Elevator
Issues Sending People up the Space Elevator
Geosynchronous
Orbital Debris
Radiation
Anders Jorgensen et. al., Acta Astronautica 60 (2007) 198 – 209
Engineering (Thermal, activities,…)
Beyond Earth orbit
Fast transit to Mars
SE capabilities allows heavily-shielded stations
Outer radiation belt
Inner radiation belt
Orbital Debris

---
Debris
Debris
Orbital debris fluxes are known pretty well
If we travel at 200km/hr with a critical volume represented by a 3m radius sphere then 1:1,000,000 trips up the elevator will be hit by a 1 cm or larger object

---
Engineering (Thermal, Activities,…)
Engineering (Thermal, Activities,…)
Comfort of people
Amount of space
Temperature control
Entertainment

---
Radiation
Radiation
In 30 days astronauts can get:
25 rem in organs
100 rem in eyes
150 rem in skin
Possible effects of short term dosage:
0-50 rem possible blood changes
50-100 radiation sickness in 5%-10% of people
1 rad in electrons is ~1 rem
1 rad in protons is ~2 rem
total
electrons
10 - 100 MeV protrons
Jorgensen
*assumes 200km/hr max travel rate

---
Increasing the Travel Speed
Increasing the Travel Speed
Total@200km/hr
Total@400km/hr

---
Intrinsic Shielding
Intrinsic Shielding
Climber mass: 13 tons
Payload mass: 7 tons
If the volume is a sphere with 3m radius
Average shielding of payload mass is 6.2 g/cm2 assuming only payload shielding
Average shielding of payload mass is 17.7 g/cm2 assuming payload and climber shielding
Intrinsic shielding is not uniform.
If payload is part shielding designed well then an effective shielding of 5 - 10 g/cm2 is reasonable
With proper design and a willingness to accept astronaut dose levels we are about there.

---
Active Shielding
Active Shielding
Geosynchronous
Radiation dose is from charged particle trapped in the Earth’s magnetic field.
Radiation does not come from cones in the direction of the Earth’s magnetic field
Charged particles can be reflected by a magnetic field
Outer radiation belt
Inner radiation belt

---
Designing a Climber
Designing a Climber
Up
Earth’s magnetic field
No radiation from this direction
No radiation from this direction
End view
Side view

---
Active Shielding
Active Shielding
Jorgensen
To be effective the magnetic dipole must reflect up to 100MeV protons
A dipole equivalent of 4e6 coils*Amps required to reflect 100 MeV protons
No secondary radiation production

---
Required Magnet (1)
Required Magnet (1)
KSTAR TF magnet: 56 turns, 35.2kA =>1.9e6 coils*amps

---
Required Magnet (2)
Required Magnet (2)
K-500 cyclotron magnet: 800A, 2200turns, 1.4 tons => 1.8 coil amps

---
Adding Plasma
Adding Plasma
Up
Earth’s magnetic field
Adding and trapping positively-charged particles to the magnetic field also slows down the incoming particles and makes them easier to stop.

---
The Flip Side
The Flip Side
Beyond GEO the situation changes
The SE allows construction of heavily shielded facilities in space
The elevator can throw cargo and astronauts to the Moon and Mars at high speeds - several times faster than rockets.

---
Not Yet Done
Not Yet Done
Good but not done
These have been average fluxes so people could still be in danger from solar storms and times with unique activity
Better studies of the full system are required

---
Space Elevator Wiki
Space Elevator Wiki
Wiki developed to initiate collaborative work on the space elevator
Includes:
Baseline Elevator
Major and minor development issues
Software to assist development work
Just finishing set-up and ready for collaborators:	www.spaceelevatorwiki.com

---
Summary
Summary
Space is dangerous
With a mixture of passive shielding, intrinsic shielding, speed of transit and active shielding the radiation hazard for people on the space elevator can be mitigated